## Slide 1
STRATA TITLE SEMINAR & WORKSHOP
BRUNEI DARUSSALAM
16 – 18 FEBRUARY 2019

## Slide 2: STRATA DEVELOPMENT – ROLES OF SURVEYORS
SALE OF PROPERTY
Preparation of Sales Agreement Plan;
The Sales Agreement Plan must identify conclusively the strata unit sold and acceptable by the Registrar of Titles for the lodging of caveats.
b) Computation of Schedule of Share Values;
Prior to selling the strata development, the developer must obtain approval of the schedule of share values from the Commissioner of Buildings. The Registered Surveyor is required to compute and submit the schedule of share values for approval.
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Notes: rightd

## Slide 3: STRATA DEVELOPMENT – ROLES OF SURVEYORS
SALE OF PROPERTY
c) Calculation and Confirmation of Strata Areas;
The Controller of Housing requires the developer to provide the purchasers a certificate of strata area duly endorsed by a Registered Surveyor. The Registered Surveyor has to ensure that as accurate an area is given based on calculation from the approved building plan.
d) Estimate the Survey Fees
The estimated survey fees, for inclusion in the standard Sales and Purchase Agreement, is provided by the Registered Surveyor. A certificate of the actual survey fees payable will be issued after the approval of the strata subdivision.
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Notes: rightd

## Slide 4: STRATA DEVELOPMENT – ROLES OF SURVEYORS
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
REGISTRATION OF PROPERTY
Land and Strata Subdivisions;
Under the planning guidelines, the Registered Surveyor is required to submit land and strata subdivision applications to the URA for approval. The strata subdivision application can only be made after the building has reaches the roof level. In practice, as the external building works are far from completed and amended building plans are not available, submission is often made near to the temporary occupation stage. On receipt of the submission, the URA will evaluate the proposal on the planning requirement and consult the relevant departments for their comments and clearance. The departments consulted are the Registry of Titles, Land Office, Survey Department, LTA, MOE, Parks and Recreation Department. The Registered Surveyor will have to deal with these departments on any comments or requirements. The URA will issue provisional permission if there are no major objection to the proposal. The final permission will be released on compliance with all comments/requirements.
.
Notes: rightd

## Slide 5: STRATA DEVELOPMENT – ROLES OF SURVEYORS
REGISTRATION OF PROPERTY
Land and Strata Subdivisions (cont’d)
In the process of strata subdivision application, the Registered Surveyor is required to:
    survey and prepare the proposal plans;
    define and edge the strata boundaries on the building plans;
    submit the proposal to the Chief Planner, URA for approval;
    liaise with the relevant departments for compliance of their technical requirements;
    resubmission of schedule of share value if there are any amendment.
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Notes: rightd

## Slide 6: STRATA DEVELOPMENT – ROLES OF SURVEYORS
REGISTRATION OF PROPERTY
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
b) Strata Title Plan (STP)
The Registered Surveyor must check that the following conditions are satisfied when preparing the STP.
    that the building comprising the strata units must be existing and must stand within the lot/plot as indicated on the approved plan;
    that the number of storey and the number of strata units in such building must tally with that stipulated on the approved plan;
    that the building does not encroach into any adjacent lot.
Notes: rightd

## Slide 7: STRATA DEVELOPMENT – ROLES OF SURVEYORS
REGISTRATION OF PROPERTY
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
c) Strata Survey
Strata survey consists of two parts:
    Survey of as-built building
All buildings must be surveyed accurately to establish their correct position and shape and to check for any encroachment onto neighbouring lots.
Notes: rightd

## Slide 8: STRATA DEVELOPMENT – ROLES OF SURVEYORS
REGISTRATION OF PROPERTY
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
c) Strata Survey (cont’d)
    ii) Survey of individual strata units
Linear dimensions of individual strata unit and common properties are measured by linen tape to determine the strata boundaries.
From the measured dimensions and compilation from approved building plans, Strata Certified Plans are drawn. Strata areas are scaled from these accurate plans. The boundaries and areas shown are final and on approval by the Chief Surveyor supersede any provisional plans prepared for the same building.
Notes: rightd

## Slide 9: STRATA DEVELOPMENT – ROLES OF SURVEYORS
REGISTRATION OF PROPERTY
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
c) Strata Survey (cont’d)
    ii) Survey of individual strata units
Linear dimensions of individual strata unit and common properties are measured by linen tape to determine the strata boundaries.
From the measured dimensions and compilation from approved building plans, Strata Certified Plans are drawn. Strata areas are scaled from these accurate plans. The boundaries and areas shown are final and on approval by the Chief Surveyor supersede any provisional plans prepared for the same building.
Notes: rightd

## Slide 10: STRATA DEVELOPMENT – STRATA SURVEY
FIELD SURVEY PROCEDURES
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Accuracy of linear measurements
i) Every strata lot shall be surveyed and the linear measurements of the survey rounded off to the nearest centimetre.
ii) The total & internal length and width of the strata lot shall to be measured. The physical height shall be measured.
(b) Use of reflector-less total station
The use of reflector-less total station for strata survey is allowed. The field data collected shall be submitted on ASCII format for submission to Chief Surveyor.
Notes: rightd

## Slide 11: STRATA DEVELOPMENT – STRATA SURVEY
FIELD SURVEY PROCEDURES
DARUSSALAM, 16 – 18 FEB 2019
All field recordings are to be entered in the Field Detail(FD) pages. All FD pages shall be drawn on A4 size with 20 mm margin (border edged in 4 point line) on all sides The first CPST No. of each job will be used as the FD No. To minimize information shown on FD, the following are not required to be shown on FD since these items are already shown on CPSTs :
i. Site Plan showing the land lot ,area, boundaries, peripheral ground details and house number/s with building outline;
ii Plan schedule and legend statement, i.e. house numbers, land lot and approved Certified Plan(CP) on where the building sits and , in the case of a strata subdivision and/or amalgamation, the new strata lot numbers;
iii. Elevation Sketch depicting stratum heights and where applicable, tabulation of strata/accessory lot numbers to their respective flat unit numbers and tabulation of accessory lots made appurtenant to respective strata lots;
Notes: rightd

## Slide 12: STRATA DEVELOPMENT – STRATA SURVEY
FIELD SURVEY PROCEDURES
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Unit numbers to be entered in the FD for all the strata lots in the storey plan (non– typical and typical storey plan).
Survey of buildings
i. The building comprising the strata lots shall be fixed directly in relation to the boundaries of the lot unless ground circumstances do not permit such fixing, and all common properties which encroach onto adjacent land shall be surveyed.
ii Strata survey for subdivision of building will require a resurvey of the land lot in situation where there is no subdivision of the land lot consequent to the development.
Notes: rightd

## Slide 13: STRATA DEVELOPMENT – STRATA SURVEY
FIELD SURVEY PROCEDURES
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
(f) Identical strata lots
Where strata lots on the same storey or on different storey of a building are identical, only one such storey shall be depicted in the field book complete with dimensions, and all pages bearing diagrams of identical strata lots shall contain the following statement:
“All strata lots including those shown as ‘similar’ herein have been entered into and all relevant measurements have been fully made.”
(g) Strata lots involving land
Where the strata lots involve land, they shall be demarcated with the approved survey marks on the ground.
Notes: rightd

## Slide 14: STRATA DEVELOPMENT – STRATA SURVEY
FIELD SURVEY PROCEDURES
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Strata boundaries
Unless otherwise stipulated on the strata certified plan, the common boundary of any lot with another lot or with the common property shall be the centre of the floor, wall or ceiling, as the case may be.
Strata boundaries intended not to follow the centre of the floor, wall or ceiling, shall be in accordance with the subdivision plans as approved/authorised by the Chief Planner. The same statement must be stipulated in the field notes and plans.
Notes: rightd

## Slide 15: STRATA DEVELOPMENT – STRATA SURVEY
FIELD SURVEY PROCEDURES
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Certification
The first diagram page of the field notes of every survey shall bear the Registered Surveyor’s certification with entries of his name and date. The certification shall read as follows:
“I, ..................................................................................... , a surveyor registered under the Land Surveyors Act (Cap. 156), certify that these field notes and diagrams on pages ......... to ............... are a correct and complete record of the survey done by me, or under my immediate personal direction and supervision, in strict compliance with the Boundaries and Survey Maps (Conduct of Cadastral Surveys) Rules 2005 (G.N. No. S 155/2005). “
Registered Surveyor (Digitally Signed)
Notes: rightd

## Slide 17
Example of STP

## Slide 20
SEE SENG GUAN
SENIOR CONSULTANT, LAND SURVEY
SURBANA JURONG CONSULTANTS PTE. LTD
STRATA DEVELOPMENT – ROLES OF SURVEYORS
STRATA TITLE SEMINAR & WORKSHOP, BRUNEI DARUSSALAM, 16 – 18 FEB 2019
Notes: rightd